## Slide 1: Advanticsys
Weekly update – 24/03/2023
Topics to discuss:
Approval of detection process
Proposal on final product/summary
Discussion to understand data

## Slide 2: Abnormal detection process
Assumptions:
Data available is on an inverter basis
Solar panels with same specifications relate to each inverter. (By this we mean the configuration of each inverter is identical)
The tolerance for considering abnormality is set to 5%. (Please advise us if this is not acceptable)
Solar panels at the start are non faulty ones.
Compare production in each inverter – check performance vs Average
Abnormal(>5%)
Check performance vs expectation based on UV/Temp
Abnormal(>5%)
Check performance vs past energy generation (identify patterns over time)
Within expectation
Normal
Within average
Normal
Off track
List as abnormal
Follow the pattern
Normal
Step 1
Step 2
Step 3

## Slide 3
100kwh
80kwh
100kwh
95kwh
100kwh
100kwh
110kwh
105kwh
100kwh
100kwh
Daily/Minute
22/03/2023
Irradiation/Temp By Inverter
Act v Prediction by inverter
Inverter 1 performance
01/01/2023 – 01/03/2023
No. | Act | Average | Var % | Pred | Var % | Capacity | Var % | result
Inv 1 | 100kwh | 100kwh | 0 | 100kwh | 0 | 95kwh | < 5% | normal
Inv 2 | 80kwh | 100kwh | 20% | 100kwh | 20% | 90kwh | 10% | abnormal
Abnormal Inverters require investigation
Step 1a – show actual number, highlight inverter with less power
Step 1b – show irradiation/temp for each inverter, highlight inverter overheat ….
Step 2 – predict power generation performance based on actual (live)irradiation/temp and other factors
Step 3 – predict performance overtime, compare with actual power generation
Final step – conclusion
No prediction in step 1, just visual summary for actual/live data

## Slide 4: Questions
Compare irradiance/temp vs energy generated
  Inside or outside?
Compare production in each inverter
  Which number to use

## Slide 5: Questions in Dataset
Which energy number in dataset to monitor
  Act_Power - kw
  Today_energy – kwh
Status per inverter meaning
Temp and irradiance from 2 weather monitoring stations
  Are they inverter temp or outside temp?