## Slide 1: Advanticsys
Weekly update – 14/04/2023
Topics to discuss:
Input Data
Output Data (reporting interval and key measure)
How to use irradiance/temp data
Rules to remove outliers

## Slide 2: Input data
Energy data – Either Today_Energy or Total_Energy for each inverter
Temperature:
  inverter readings
  WMS reading
    WMS01 for Inverters 01 – 05
    WMS02 for Inverters 06 – 10
WMS irradiance:
  WMS01 for Inverters 01 – 05
  WMS02 for Inverters 06 – 10

## Slide 3: Input data

## Slide 4: Output (Reporting interval and measure)
Energy data
  Quarterly energy generation
    Total MWh generated
    Average MWh per minute in each quarter
  Daily energy generation
    Total MWh generated
    Average MWh per minute on each day

## Slide 5: Correlating irradiance/temp data
Option 1:
  Use average irradiance/temp in each reporting interval
Option 2:
  Use high & low irradiance/temp in each reporting interval

## Slide 6: Remove outlier – Today_Energy
Step 1 - Remove 0 and negative readings
Step 2 - Remove readings higher than upper limit
  Around 4000 MWh (2020)

## Slide 7: Remove outlier – Temperature (Inverter Readings)
Step 1 - Remove readings lower than lower limit
  31 degree for inv01 (2020)
Step 2 - Remove readings higher than upper limit
  57 degree for inv01 (2020)

## Slide 8: Remove outlier – Temperature (WMS Readings)
Step 1 - Remove readings lower than lower limit
  15 degree for wms01 (2020)
Step 2 - Remove readings higher than upper limit
  41 degree for wms01 (2020)

## Slide 9: Remove outlier – Irradiance (WMS Readings)
Step 1 - Remove readings less than 0
Step 2 - Remove readings higher than upper limit
  1500 W/m^2 (2020)

## Slide 10: Data output for inv01 for 2020
By Minute
By Quarter
Average for each quarter
Energy recording at beginning and end of each quarter
Avg energy generation per minute

## Slide 15: From last meeting: Identified required files and separated them
The following files are considered for now: today_energy_data, total_run_data, today_run_data, total_energy_data, temp_data, irradiance_data, temp_data
For each year, overall, 54 files are there.
All files are having the same structure. We will be combining the data on an inverter basis.

## Slide 16: From last meeting: How should be the frequency of the reporting be?
The data available is on a minute by minute basis.
Planning to group the data with a 15 minute frequency.
Average values will be considered for this 15 min frequency.